## Slide 1
OXOT · OT SECURITY ENGINEERING
How we build a Cyber Digital Twin
Three phases, two client workshops, three floor walks — from the client's own documentation to a defensible IEC 62443 determination.
One dataset produces every artifact, so a change in the field propagates everywhere at once.
Notes: Three phases, two workshops, three floor walks. The point of the whole method: one dataset produces every artifact.

## Slide 2
The process, end to end
OXOT · CYBER DIGITAL TWIN
The model is built from documentation, corrected against the physical plant, then loaded with safety and reliability data before any control is recommended.
1
Build the model
Derive the asset list, establish every connection, classify services and protocols, separate routable from hardwired.
ARTIFACTS
Asset register · Connection graph · 3D model
W1
Workshop 1
Review the model with the client, walk the floor, correct to as-is, then frame the threat through ATQ.
ARTIFACTS
Initial SL-T zones and conduits · SIL items marked
2
Load consequence
Attach failure modes to assets, encode redundancy from the design, make every pathway traceable to a physical outcome.
ARTIFACTS
Consequence model · MoR and operating modes
W2
Workshop 2
Show threat actors and pathways on the model, trace to loss, then test gaps against ALARP / SFAIRP.
ARTIFACTS
SL-C rationale · ZCR diagram
3
Verify & report
Raise fidelity with configurations and bills of material, walk the floor again, then deliver the roadmap.
ARTIFACTS
NOW / NEXT / NEVER · Target architecture · Readout
FLOOR WALK 1 — CONFIRM AS-IS
FLOOR WALK 2 — CONFIRM HIGH-FIDELITY MODEL
Notes: Walk left to right. Orange columns are the two client workshops. The floor walks sit under W1 and Phase 3.

## Slide 3
1
Build the model
Documents in, queryable model out. Nothing is asked of the client team at this stage.
INPUTS
High-level design (HLD)
Detailed level design (DLD)
Interface control document (ICD)
OT equipment schedules
Descriptions and narratives
WHAT WE DO
Derive the asset list from documentation
Establish every connection between assets
Classify services — what flows
Classify protocols — how it is carried
Separate routable from hardwired
ARTIFACTS
Asset register
Connection graph
Service and protocol inventory
3D model of the facility
Notes: Nothing is asked of the client team yet. Separating routable from hardwired is the step most assessments skip.

## Slide 4
W1
Workshop 1 — Initial Risk Assessment
Review the model, walk the floor, correct to as-is, then frame the threat.
INPUTS
The model from Phase 1
Client review and corrections
Sector threat intelligence
Client, equipment and facility profile
Geography
WHAT WE DO
Review the model with the client
Walk the floor — confirm against as-is
Adjust where documents and plant disagree
Frame the threat landscape. TS 50701 uses worst case; we apply comparative sector threats through ATQ
Mark SIL-rated items
ARTIFACTS
As-is corrections
Initial SL-T zones and conduits
Asset registry, SIL items marked
Notes: TS 50701 works from worst case. ATQ gives comparative sector threat instead — defensible rather than hypothetical.

## Slide 5
2
Load consequence
The safety and reliability teams' own work, built into the model.
INPUTS
Safety team: FMEA, hazard log
Safety critical item list
Reliability critical item list
ConOps
Minimum operating requirements
WHAT WE DO
Attach failure modes to assets
Build impacts and consequences into the model
Encode redundancy from the design, not from feed count
Encode MoR thresholds and operating modes
Make a pathway traceable to a physical outcome
ARTIFACTS
Failure modes on assets
Consequence model
MoR and operating modes
Notes: Redundancy is encoded from the design, not inferred from feed count — that distinction matters and clients notice it.

## Slide 6
W2
Workshop 2 — Risk Alignment
Show the consequence, then agree what is reasonable to do about it.
INPUTS
Consequence-loaded model
TACAM — typical vulnerabilities by equipment class
Threat actor profiles from ATQ
SL-T from Workshop 1
WHAT WE DO
Show threat actors and pathways on the model
Trace to fat-tail loss, critical loss and safety consequence — our own ALE model
Review controls the SL-T ratings require, and why, grounded in pathway and consequence
Test architectural gaps against ALARP / SFAIRP for a reasonable SL-C
Draw the flat network view of the 3D model
ARTIFACTS
Threat pathways and consequence
SL-C rationale
ZCR diagram — zones and conduits
Notes: This is where controls get argued from the pathway and the consequence at the end of it, not from a checklist.

## Slide 7
3
Verify & report
Raise the model to the fidelity of the actual facility, then deliver the roadmap.
INPUTS
Samples and configurations
SBOMs and HBOMs
Switch and firewall configurations
SL-C and security requirements by zone
WHAT WE DO
Enter SL-C and requirements per asset by zone
Raise model fidelity to the actual facility
Walk the floor again with the improved model
Gap analysis SL-C against SL-A
Build the target reference architecture
ARTIFACTS
NOW / NEXT / NEVER report
Target reference architecture (IEC 62443)
SL-C to SL-A gap analysis
Roadmap, priority actions, quick wins
Executive readout + long-form report
Notes: Second floor walk is with the high-fidelity model. This is what makes the NOW/NEXT/NEVER call defensible.

## Slide 8
Where the outputs go
One dataset, every team. The usual failure of an OT assessment is that each team receives a different document and none of them reconcile.
Executives and risk
Executive briefing and readout. Input to the organisational risk ledger where the sponsor is organisational. Consequence tied to numbers, top down.
Facility managers
SecRAC for the facility. Zone and conduit responsibilities, and the controls that apply to plant they operate day to day.
Safety and reliability
Reliability and safety critical items returned to the hazard log, so the safety team's own artifact stays current.
IT, OT, controls, network, operations, security
The full detailed report aligned to IEC 62443 and CLC/TS 50701, and the model itself. Bottom-up engineering view that earns trust.
Notes: The usual failure is each team getting a different document. Here every team reads the same model through its own view.

## Slide 9
THE OUTCOME
A formal, defensible process and artifact set for an IEC 62443 determination of SL-C — including where it is negotiated down to SL-A.
Consequence-driven reporting from the top down, an engineering and operations view from the bottom up, and one common set of information for every team.
OXOT · OT SECURITY ENGINEERING
info@oxot.nl
Notes: Close on the defensibility point — including where SL-C is negotiated down to SL-A, which is the honest case.